## Slide 1: Eyelib Eye Tracker Library
Nathan Lucas

## Slide 2: Eyelib
OneNote
  Eyelib Library
Documentation
  file:///D:/Lucas/projects/eyetracking/eyelib/doc/html/index.html
As of 14 Jan 2017

## Slide 3: Modules
Module | Capability | Interface
calib | Eye tracker calibration results Overall calibration state and error Calibration point state, coordinates, error, and sample standard deviation | calibration.hpp
gaze | Eye gaze data | gaze.hpp
 | Fixation detection algorithms Dispersion threshold Velocity threshold | gaze/dispersion_threshold.hpp gaze/dispersion_threshold.hpp
 | Eye tracking metrics Blink time, fixation time, saccade distance, pupillometry | gaze/metics.hpp
 | Point cluster Group of gaze point coordinates Not currently used by any component of Eyelib | gaze/point_cluster.hpp
screen | Screen-related data structures and functions 2D point, gaze target point, gaze target duration, RGB color, screen parameters | screen.hpp
tracker | Core eye tracker functionality | tracker.hpp

## Slide 4
Start: Tracker Client (EyeTribeUIWin.exe)
Start: Tracker Server (EyeTribe.exe)
Initialize Hardware
Heartbeat
Calibration

## Slide 5: Eyelib API (v2)
analysis
tracker
Tracker
Calibrator
Calibration
DispersionThreshold
GazeData
Target
TargetArray
ServerState
DeviceState
ScreenState
+ register_handler ( callback : calib_handler )
+ register_handler ( callback : gaze_handler )
+ start ( ... )
+ register_handler ( callback : state_handler )
+ state ( ) const : State
+ calibrate ( ... )
ScreenListener
DeviceListener
ServerListener
GazeListener
CalibrationListener
CalibratorListener
Point2D
EyeData
VelocityThreshold
gazeapi
console
centroid()
mean()
datalog
Console
GazeOut
DataLog
State
+ window ( ... )
+ window ( ... )

## Slide 6: Calibration

## Slide 7: Eye Tracker Calibration
Accuracy and error
tan(θ) = e/d
  θ is angular accuracy
  e is on-screen error
  d is distance to screen
The Eye Tribe Tracker product documentation
  Instructs to center user in front of the monitor at a distance of 45-75 cm (17.7-29.5 in)
  Reports calibrated system calculates eye gaze coordinates with an average accuracy of approximately 0.5 to 1°
  Reports average error of 0.5 to 1 cm (0.2 to 0.4 in) at 60 cm (23.6 in) from the screen/tracker

## Slide 8: Calibration Point Results
gray: uncalibrated
red: recalibrate (> 1.5°)
orange: poor (≤ 1.5°)
yellow: moderate (≤ 1.0°)
light green: good (≤ 0.7°)
dark green: great (≤ 0.5°)
Rating Scale and Accuracy
Components
binocular
right eye
left eye
Example
good
moderate
great

## Slide 9: Calibration Criteria
Each Calibration Point
light or dark
green
green or
yellow
Overall Results
dark
green
light or dark
green

## Slide 10: Gaze Target

## Slide 11: Gaze Target
start()
point_start()
point_end()
advance()
handler
handler
handler
handler
delay_ms
duration_ms
0
delay_ms
calibration_
point_start()
calibration_
point_end()
calibration_
start()
Response:
start
Response:
point_start
Server
Response:
point_end
Server
Server
Enter key
Fixation Target
Calibration

## Slide 12: Fixation Algorithms

## Slide 13
?
?
?
?
F
F
F
?
F
F
F
F
?
?
?
?
?
?
?
?
?
?
?
?
?
?
F
F
F
?
fixation
F
F
F
F
add point
F
F
F
check dispersion
F
F
F
F
F
F
F
F
?
S
?
?
S
?
?
S/F
F
F
F
F
F
?
S
S
S
S
S
S
add point
add point
add point
add point
add point
add point
add point
add point
add point
saccade
S
S
S
S
S
S
S
S
S
S
S
fixation
F
F
F
check dispersion
check dispersion
check dispersion
check dispersion
check dispersion
check dispersion

## Slide 14
?
?
?
S
?
?
?
S
S
?
?
?
?
?
?
F
F
F
?
saccade
S
S
S
add point
S
?
?
check dispersion
S
S
?
?
S
S
S/F
F
F
F
F
F
?
add point
add point
add point
add point
add point
fixation
F
F
F
check dispersion
check dispersion
check dispersion
?
?
add point
S
?
?
?
S/F
F
F
add point
S
S
saccade
S
S
F
F
F
?
add point
check dispersion

## Slide 15: Metrics

## Slide 16: Blink State
!blink
record blink
start time
eyes
closed
record blink
duration
blink
start
eyes
closed
eyes
open
eyes
open
record blink
interval

## Slide 17: Metrics
Test workload
sensitivity
Test fixation
accuracy
Timestamp
(date and time)
Timestamp
(millisecond)
Tracking
State
Fixation
(true/false)
Raw Gaze
Point
Smoothed
Gaze Point
DT Fixation
(true/false)
VT Fixation
(true/false)
DT Fixation
(true/false)
VT Fixation
(true/false)
Test and
compare
fixation
detection
algorithms
Blink
(true/false)
Blink
Duration
Blink
Interval
Target
Sequence
(true/false)
Target Point
(x, y)
Target Active
(true/false)
Fixation
Duration
Fixation
Interval
Saccade
Distance
(pixel2)
Left Pupil
Coordinates
Right Pupil
Coordinates
Left Pupil
Size
Right Pupil
Size
Average
Pupil Size
Key
Raw Data
Derived
Test Data
Metrics
Lighting
Condition
Workload
Condition
?
?
?
?
?
?
Test blink
detection