## Slide 1: Eyelib Fixation Test
Nathan Lucas

## Slide 2: Calibration

## Slide 3: Eye Tracker Calibration
Accuracy and error
tan(θ) = e/d
  θ is angular accuracy
  e is on-screen error
  d is distance to screen
The Eye Tribe Tracker product documentation
  Center user in front of the monitor at a distance of 45-75 cm (17.7-29.5 in)
  Eye Tribe server reports calibrated system calculates eye gaze coordinates with an average accuracy of approximately 0.5 to 1°
  Eye Tribe server reports average error of 0.5 to 1 cm (0.2 to 0.4 in) at 60 cm (23.6 in) from the screen/tracker

## Slide 4: Calibration Point Results
gray: uncalibrated
red: recalibrate (> 1.5°)
orange: poor (≤ 1.5°)
yellow: moderate (≤ 1.0°)
light green: good (≤ 0.7°)
dark green: great (≤ 0.5°)
Rating Scale and Accuracy
Components
binocular
right eye
left eye
Example
good
moderate
great

## Slide 5: Calibration Criteria
Each Calibration Point
light or dark
green
green or
yellow
Overall Results
dark
green
light or dark
green

## Slide 6: Preliminary Fixation Study

## Slide 7: Preliminary Fixation Study
Exploratory data analysis
  Scatter plots
Fixation point accuracy
Determine appropriate parameters for dispersion threshold (DT) and velocity threshold (VT) fixation detection algorithms
  Window size – number of contiguous points for which to compute dispersion
  Maximum dispersion of fixation points
  Maximum displacement between fixation points
Test metrics for fixations on object (target)
  Count of fixations
  Average duration
  Interval between fixations

## Slide 8: Exploratory Data Analysis
Gaze points during
active target
Gaze points
during fixation
Filter: active = TRUE, ET = TRUE
Filter: ET = TRUE
Filter: active = TRUE
All gaze points
(fixations and saccades)
Filter: none
Gaze points during active
target and fixation
Some fixations were not
on or during active target
As expected, high density
of fixations near targets
As expected, high density
of gaze points near targets
Smoothed gaze points
reveal saccade paths
Data set: 20170217T174030-fixation

## Slide 9: Fixation Point Accuracy
Data set: 20170217T174030-fixation
Target |  |  | Count of points | Average raw gaze |  |  |  |  | Average smoothed gaze |  |  |  | 
 |  |  |  | Gaze point |  | Percent error |  | Pixel error | Gaze point |  | Percent error |  | Pixel error
ID | x | y |  | x | y | x | y |  | x | y | x | y | 
0 | 102 | 102 | 182 | 80.50 | 107.65 | 21.1% | 5.5% | 22.23 | 77.50 | 105.97 | 24.0% | 3.9% | 24.82
1 | 640 | 102 | 183 | 616.44 | 112.93 | 3.7% | 10.7% | 25.97 | 615.50 | 116.04 | 3.8% | 13.8% | 28.24
2 | 1178 | 102 | 182 | 1151.23 | 107.88 | 2.3% | 5.8% | 27.41 | 1147.84 | 111.52 | 2.6% | 9.3% | 31.63
3 | 102 | 512 | 182 | 71.11 | 517.19 | 30.0% | 1.0% | 31.32 | 71.98 | 519.14 | 29.4% | 1.4% | 30.86
4 | 640 | 512 | 182 | 613.30 | 516.38 | 4.2% | 0.9% | 27.05 | 611.00 | 532.62 | 4.5% | 4.0% | 35.58
5 | 1178 | 512 | 179 | 1156.58 | 516.63 | 1.8% | 0.9% | 21.92 | 1153.39 | 520.27 | 2.1% | 1.6% | 25.96
6 | 102 | 922 | 182 | 89.23 | 906.73 | 12.5% | 1.7% | 19.90 | 93.53 | 910.16 | 8.3% | 1.3% | 14.56
7 | 640 | 922 | 181 | 629.65 | 920.21 | 1.6% | 0.2% | 10.50 | 632.79 | 921.12 | 1.1% | 0.1% | 7.26
8 | 1178 | 922 | 181 | 1129.59 | 898.92 | 4.1% | 2.5% | 53.63 | 1129.42 | 899.33 | 4.1% | 2.5% | 53.61
Avg. | 640 | 512 | 1634 | 613.98 | 510.87 | 4.1% | 0.2% | 26.05 | 613.46 | 514.39 | 4.1% | 0.5% | 26.65
As expected, average raw and smoothed
gaze error values are very consistent

## Slide 10: Fixation Point Accuracy
Screen pixels per inch (PPI)
  Screen resolution:
  1280 pixels / 14 13/16 in = 86 PPI
  1024 pixels / 11 7/8 in = 86 PPI
  Screen diagonal:
  (12802 + 10242)1/2 / 19 in = 86 PPI
  On-screen measurement:
  200 pixels / 25/16 in = 86 PPI
Accuracy
tan(θ) = e/d
  θ is angular accuracy
  e is on-screen error
  d is distance to screen (24.5 in)
Raw gaze
  e = 26 pixels / 86 PPI = 0.30 in
  θ = tan-1(0.30/24.5) = 0.70°
Smoothed gaze
  e = 27 pixels / 86 PPI = 0.31 in
  θ = tan-1(0.31/24.5) = 0.72°
Data set: 20170217T174030-fixation

## Slide 11: Dispersion and Displacement During Active Target
Data set: 20170217T174030-fixation
Target |  |  | Count of points | Average raw gaze |  | Average smoothed gaze | 
ID | x | y |  | Dispersion (pixels) | Displacement (pixels) | Dispersion (pixels) | Displacement (pixels)
0 | 102 | 102 | 182 | 90.88 | 40.91 | 14.17 | 0.98
1 | 640 | 102 | 183 | 101.40 | 44.60 | 17.33 | 1.34
2 | 1178 | 102 | 182 | 80.65 | 34.39 | 17.40 | 1.62
3 | 102 | 512 | 182 | 106.04 | 44.77 | 28.06 | 6.62
4 | 640 | 512 | 182 | 87.48 | 37.92 | 11.51 | 1.63
5 | 1178 | 512 | 179 | 80.51 | 32.77 | 12.99 | 0.93
6 | 102 | 922 | 182 | 80.06 | 29.35 | 27.54 | 0.87
7 | 640 | 922 | 181 | 57.59 | 26.31 | 11.00 | 0.61
8 | 1178 | 922 | 181 | 104.76 | 43.55 | 37.41 | 16.87
Avg. | 640 | 512 | 1634 | 87.74 | 37.19 | 19.72 | 3.49

## Slide 12: All Smoothed Gaze Points
Dispersion
Displacement
The data suggest a
dispersion threshold
Fixation?
Dispersion window: 4 points
Data set: 20170217T174030-fixation
Filter: none

## Slide 13: Smoothed Gaze Points During Active Target
Dispersion
Displacement
Data filtered to show
only fixation points
while target is active
Non-fixation points,
perhaps just before
fixation is detected?
Data set: 20170217T174030-fixation
Filter: active = TRUE
Dispersion window: 4 points

## Slide 14: Smoothed Gaze Fixation Points During Active Target
Data set: 20170217T174030-fixation
Filter: active = TRUE, ET = TRUE
Dispersion
Displacement
Dispersion window: 4 points
28
5
Data filtered to show
only points while
target is active

## Slide 15: Smoothed Gaze All Fixation Points
Dispersion
Displacement
28
Higher displacement
threshold would permit
additional fixation points
observed outside the
active target durations
Data set: 20170217T174030-fixation
Filter: ET = TRUE
Dispersion window: 4 points
7

## Slide 16: All Smoothed Gaze Points
Dispersion
Displacement
28
7
Dispersion window: 4 points
Data set: 20170217T174030-fixation
Filter: none

## Slide 17: Smoothed Gaze Displacement and Dispersion
Active Target
Points
All Gaze
Points
Fixation of
Active Target
All Fixation
Points
Observed
displacement
and dispersion
thresholds
Dispersion window: 4 points
Data set: 20170217T174030-fixation

## Slide 18: Raw Gaze Displacement and Dispersion
Data set: 20170217T174030-fixation
Active Target
Points
All Gaze
Points
Fixation of
Active Target
All Fixation
Points
Displacement
and dispersion
thresholds are
less clear from
raw gaze points
Dispersion window: 4 points

## Slide 19: Dispersion Threshold
Typical maximum dispersion
  0.5° to 1°
  d · tan(θ) · p
  d = 24.5 inches to screen
  p = 86 pixels per inch (PPI)
  24.5 in · tan(0.5°) · 86 PPI = 18 pixels
  24.5 in · tan(1.0°) · 86 PPI = 37 pixels
  Observed dispersion threshold
  θ = tan-1( (28 pixels / 86 PPI) / 24.5 in) = 0.76°
Data set: 20170217T174030-fixation

## Slide 20: Dispersion and Displacement
Typical velocity threshold
  Fixation: < 100°/second → 24.5 in · tan(100°/s / 60 fps) · 86 PPI = 61 pixels
  Saccade: > 300°/second → 24.5 in · tan(300°/s / 60 fps) · 86 PPI = 184 pixels
  Observed displacement threshold
  θ = tan-1( (7 pixels / 86 PPI) / 24.5 in) · 60 fps = 11°/s
Data set: 20170217T174030-fixation

## Slide 21: Fixations on Targets
Data set: 20170217T174030-fixation
Target | x | y | Count of fixations on target | Average fixation duration (ms) | Interval between fixations (ms)
0 | 102 | 102 | 3 | 1,875 | 20,295
1 | 640 | 102 | 3 | 1,665 | 14,200
2 | 1178 | 102 | 3 | 2,420 | 32,449
3 | 102 | 512 | 3 | 2,153 | 16,316
4 | 640 | 512 | 3 | 1,686 | 16,217
5 | 1178 | 512 | 3 | 1,864 | 28,369
6 | 102 | 922 | 3 | 1,860 | 6,144
7 | 640 | 922 | 3 | 1,890 | 18,280
8 | 1178 | 922 | 3 | 1,876 | 10,222
Average |  |  | 3 | 1,921 | 18,055
Fixation durations
should be equal
to or greater than
the target active
time of 1,000
milliseconds.
An average interval of
18,000 milliseconds
would be consistent
with 9 targets and
2,000 milliseconds
per target.
Ideal count is 3, one for each
target sequence. Less than 3
represents failure to detect
fixation(s) on a target.
Greater than 3 represents
interrupted fixation(s).

## Slide 22: Preliminary Fixation Study – Summary
Exploratory data analysis provides evidence of expected observations
  Smoothed gaze points reveal saccade paths
  High density of gaze points observed near targets
  High density of fixations observed near targets
  Some fixations appear not to be on or during an active target
Fixation point accuracy
  Average error: 26-27 pixels (0.7° visual angle)
Parameters for fixation detection
  DT window size: 4 points
    Initial testing suggested 4 points would be sufficient
    Data analysis provides evidence to support
  Maximum dispersion of fixation points in DT window: 28
    Evidence implemented DT algorithm may be suitable for fixation detection
  Maximum displacement between fixation points: 7
    However, there is evidence implemented VT algorithm may not be suitable for fixation detection
Test metrics for fixations on object (target)
  Count of fixations for each target equals 3, one for each target sequence
  Average fixation duration at each target is greater than the minimum of 1,000 ms
  Interval between fixations is consistent with a sequence of 9 targets, repeated 3 times, with 2,000 ms per target

## Slide 23: Fixation Test

## Slide 24: Fixation Test Objectives
Test reliability and compare three (3) fixation detection methods
  Eye tracker fixation flag (ET)
  Dispersion threshold (DT)
  Velocity threshold (VT)
  Input smoothed gaze points to both DT and VT
  Is eye tracker fixation detection sufficient?
Measure fixation point accuracy
  Smoothed gaze point error during fixation, in pixels and degrees visual angle
  Compare with reported accuracy of eye tracker
Model the relationship between fixation metrics and attention
  May need to use a different test
  This test might be limited to assessing reliability of measurements
Capture pictures of experiment for use during dissertation defense
Fixation Test
Introduction

## Slide 25: Test Parameters
Category | Parameter | Value | Units
Fixation detection | DT sample window size | 4 | points
 | DT maximum dispersion | 30 | pixels
 | VT maximum displacement | 7 | pixels
Target duration | Before active | 750 | milliseconds
 | Active state | 750 | milliseconds
 | After active | 0 | milliseconds
Target sequence | Number of targets per cycle | 9 | targets
 | Number of target cycles | 3 | cycles
Fixations | Fixation object radius | 56 | pixels
Fixation Test
Introduction

## Slide 26: Data Analysis
Fixation Test
Introduction
File type | File name | Description
Data log | 20170310T150350-fixation-A3.csv 20170310T152053-fixation-B1.csv 2017XXXXTXXXXXX-fixation-CX.csv | Gaze and fixation data CSV files File timestamp Timestamped eye tracker, target, fixation detection, and target object fixation Summary of target object fixation for each fixation detection method
 | 20170310T150350-fix-calib-A3.csv 20170310T152053-fix-calib-B1.csv 2017XXXXTXXXXXX-fix-calib-CX.csv | Calibration results CSV files File timestamp Overall calibration results Calibration point results
Report | 20170310T150350-fixation-A3-gaze.xlsx | Scatter plots of gaze points, including animated playback
 | 20170310T152053-fixation-B1-accuracy.xlsx | Bubble chart and table of eye tracker calibrated and observed accuracy
 | 20170310T152053-fixation-B1-calib.xlsx | Bubble chart and table of eye tracker calibration accuracy
 | 20170310T152053-fixation-B1-target.xlsx | Bar and bubble charts of fixation count, duration, and interval
Analysis | 20170310T150350-fixation-A3.xlsx 20170310T152053-fixation-B1.xlsx 2017XXXXTXXXXXX-fixation-CX.xlsx | File timestamps from CSV source data
 | fixation-test.xlsx | Aggregate data analysis workbook
TBD
TBD
TBD

## Slide 27: Fixation Detection
Total count of fixation points may varying by participant, depending on the frequency and duration of fixations between active targets.
However, during active target periods the percentage of points for which fixation is detected should approach 100% and the count of fixation points should be more consistent among individual targets and participants.
Fixation Test
Objective 1

## Slide 28: Fixation Detection
Source: Analysis workbooks : fixation, compare
Target | Participant | ET = true | DT = true | VT = true | ET = DT | ET = VT | DT = VT
active = true | A | 97.8% | 94.9% | 99.8% | 93.7% | 98.0% | 95.2%
 | B | 96.6% | 92.7% | 99.2% | 92.2% | 97.4% | 93.3%
 | C | % | % | % | % | % | %
active = false | A | 53.0% | 72.0% | 79.9% | 77.7% | 73.1% | 91.4%
 | B | 53.9% | 70.8% | 81.6% | 77.3% | 72.1% | 87.9%
 | C | % | % | % | % | % | %
All points | A | 71.4% | 81.4% | 88.0% | 84.3% | 83.4% | 93.0%
 | B | 71.7% | 79.9% | 89.0% | 83.5% | 82.7% | 90.2%
 | C | % | % | % | % | % | %
Fixation Test
Objective 1
TBD
TBD
TBD
ET produces fewer
false positives (?)

## Slide 29: Smoothed Gaze Fixation Points
Source: Analysis workbooks : smoothed
ET = true
DT = true
VT = true
Participant A
Participant B
Participant C
Objective 1
Fixation Test
TBD

## Slide 30: Smoothed Gaze Saccade Points
Source: Analysis workbooks : smoothed
Participant A
Participant B
Participant C
ET = false
DT = false
VT = false
Objective 1
Fixation Test
TBD

## Slide 31: Fixation Point Accuracy
 |  |  | Smoothed gaze point error during fixation |  |  |  |  | 
Target |  |  | Displacement on screen (pixels) |  |  | Visual angle (degrees) |  | 
 |  |  | Participant |  |  | Participant |  | 
ID | x | y | A | B | C | A | B | C
0 | 102 | 102 | 20.09 | 17.81 |  | 0.55 | 0.48 | 
1 | 640 | 102 | 11.04 | 25.89 |  | 0.30 | 0.70 | 
2 | 1178 | 102 | 21.89 | 12.11 |  | 0.60 | 0.33 | 
3 | 102 | 512 | 15.25 | 28.35 |  | 0.41 | 0.77 | 
4 | 640 | 512 | 13.29 | 8.75 |  | 0.36 | 0.24 | 
5 | 1178 | 512 | 26.51 | 24.99 |  | 0.72 | 0.68 | 
6 | 102 | 922 | 16.50 | 24.45 |  | 0.45 | 0.66 | 
7 | 640 | 922 | 5.60 | 20.35 |  | 0.15 | 0.55 | 
8 | 1178 | 922 | 11.47 | 10.99 |  | 0.31 | 0.30 | 
Avg. | 640 | 512 | 15.75 | 19.25 |  | 0.43 | 0.52 | 
Source: Analysis workbooks : accuracy
Objective 2
Fixation Test
TBD
TBD
TBD
TBD

## Slide 32: Fixation Point Accuracy
Objective 2
Fixation Test
Source: Analysis workbooks : accuracy
TBD

## Slide 33: Fixation Point Accuracy
Observed fixation point error vs. calibration accuracy reported by the eye tracker
  Note: Locations of fixation test software (eyelib-test -f) gaze targets are within 1 pixel of the 3×3 array of calibration points used by EyeTribe UI (EyeTribe-UIWin)
Objective 2
Fixation Test
 |  |  | Calibration accuracy |  |  | Observed error |  |  | Percent difference |  | 
ID | x | y | A | B | C | A | B | C | A | B | C
0 | 102 | 102 | 0.33° | 0.20° |  | 0.55° | 0.48° | ° | 49% | 81% | %
1 | 640 | 102 | 0.48° | 0.29° |  | 0.30° | 0.70° | ° | 47% | 84% | %
2 | 1178 | 102 | 0.34° | 0.46° |  | 0.60° | 0.33° | ° | 55% | 32% | %
3 | 102 | 512 | 0.59° | 0.25° |  | 0.41° | 0.77° | ° | 36% | 103% | %
4 | 640 | 512 | 0.65° | 0.42° |  | 0.36° | 0.24° | ° | 57% | 55% | %
5 | 1178 | 512 | 0.60° | 0.35° |  | 0.72° | 0.68° | ° | 19% | 64% | %
6 | 102 | 922 | 0.27° | 0.05° |  | 0.45° | 0.66° | ° | 48% | 174% | %
7 | 640 | 922 | 0.24° | 0.13° |  | 0.15° | 0.55° | ° | 45% | 123% | %
8 | 1178 | 922 | 0.27° | 0.10° |  | 0.31° | 0.30° | ° | 14% | 100% | %
Avg. | 640 | 512 | 0.42° | 0.25° |  | 0.43° | 0.52° | ° | 2% | 71% | %
 |  |  |  | ° |  |  | ° |  |  | % | 
TBD
TBD
TBD
TBD
TBD
TBD
Source: Analysis workbooks : accuracy

## Slide 34: Object Fixations
Fixation duration
  The average fixation duration for each target should be equal to or greater than the target active duration of 750 ms. If the participant immediately fixated the target when it appeared until the moment it disappeared, the fixation duration would be the pre-active plus active target durations:
  750 + 750 = 1,500 ms
  Because the participant may fixate near a target location even when the target is not present, the fixation duration may even exceed 1,500 ms. However, the average per target and overall average should generally be in the range of 750-1,500 ms.
Fixation interval
  Because the target order is randomized for each target cycle, the observed fixation interval is not expected to be the same for each target. Furthermore, the average of all target intervals may vary significantly between participants due to variability in the delay between the target cycles. However, the average of all target values for each participant may provide some confirmation that the fixation interval metric functions as anticipated. The theoretical average interval is a function of the number of targets and the duration of each target:
  tint = 9 targets · 1,500 ms = 13,500 ms
Objective 3
Fixation Test

## Slide 35: Object Fixations
Model the relationship between fixation metrics and attention
  Possible fixational measures of attention include the count of fixations of an object; the peak, average, or sum total fixation time duration; and response time until the first fixation of an object
Approach
  Assess the consistency of fixation count and duration(?)
  May need to use a different test...
 | Count of fixations on object |  |  | Average fixation duration (ms) |  |  | Average fixation interval (ms) |  | 
 | Participant |  |  | Participant |  |  | Participant |  | 
 | A | B | C | A | B | C | A | B | C
ET | 3.1 | 3.1 |  | 1,557 | 1,408 |  | 13,472 | 13,312 | 
DT | 5.1 | 5.2 |  | 963 | 827 |  | 7,435 | 7,610 | 
VT | 3.0 | 3.2 |  | 1,610 | 1,396 |  | 13,472 | 13,282 | 
Average | 3.7 | 3.9 |  | 1,377 | 1,210 |  | 11,460 | 11,402 | 
Source: Analysis workbooks : target
Objective 3
Fixation Test
TBD
TBD
TBD
ET and VT produce
more consistent and
accurate fixation
counts and durations
than DT (?)
...or...
Could just be DT
is more sensitive
than ET and VT (?)

## Slide 36: Object Fixations
Objective 3
Fixation Test
Compare fixation count and duration
results from ET, DT, and VT fixation detection
Source: Analysis workbooks : target

## Slide 37: Test Bed Pictures
Objective 4
Fixation Test
TBD

## Slide 38: Fixation Test Summary
Fixation detection
  Comparable performance?
  Hypothesis: DT and VT work, but offer no apparent advantage over ET
Measure fixation point error
  Average error: XX pixels (X.X° visual angle)
Model the relationship between fixation metrics and attention
  Fixations on object (target)
    Count of fixations for each target equals 3, one for each target sequence
    Average fixation duration at each target is greater than the minimum of 1,000 ms
    Interval between fixations is consistent with a sequence of 9 targets, repeated 3 times, with 2,000 ms per target
Capture pictures of experiment for use during dissertation defense
Fixation Test
Conclusion

## Slide 39: Attention and Workload Test